## Slide 1
B-PILLER PLASTIC TRIM

## Slide 2
MASTER_SECTION

## Slide 3
DISASSEMBLE
JOIN MERGING DISTANCE 0.01
IF ANY AREA IS MISSED

## Slide 4
CREATE A POINT
CREATE A BOUNDARY
EXTRAPOLATE
EDGE FILLET 3MM

## Slide 5
OFFSET OF 2.5MM
OFFSET OF 3.5MM
SKETCH
SWEPT THE SKETCH
The plastic trim design incorporates a variable wall thickness strategy, utilizing B-surface offsets of 2.5 mm and 3.5 mm. To accommodate this variation, a smooth transient blend was modeled between the two regions, ensuring a continuous material flow and an optimal transition along the connecting surfaces.

## Slide 6
OFFSET OF 20mm
SPLIT BOTH 2.5& 3.5mm OFFSET
BLEND 2.5mm & 3.5mm OFFSET
MUTI- SETION 2.5mm & 3.5mm OFFSET & BLEND
FINAL VIEW OF B SURFACE

## Slide 7
C- SURFACE
OFFSET SURROUNDING DATA OF 0.5mm
SPLIT THE OFFSET SURFACE

## Slide 8
DEFINE A BORDERTO A -SURFACE
SWEEPT THE BORDER
JOIN C-SURFACE
BLEND THE A & B SURFACE

## Slide 9
SWEPT THE A-SURFACE BORDER
SPLIT THE SWEEP

## Slide 10
CHECK IF ANY AREA IS OPEN
CLOSE VOLUME
FINAL VIEW OF A, B& C CLOSE VOLUME

## Slide 11
DOG_HOUSE